## Slide 1: Summary of Upstream / Downstream Emissions
Upstream Emissions | kt CO2 | Downstream Emissions | kt CO2
Purchased goods & services | 10,000,000 | Investing | -
Fuel & energy related activity | 208,000 | Downstream transportation & distribution | 706,000
Upstream transport & distribution | 624,000 | Processing solid products | 10,000
Business Travel | 121,464 | Use of solid product | 80,675,000
Upstream leased asset | - | End of life treatment of solid products | 167,000
Employee commuting | 209,233 | Downstream leased assets | -
Capital goods | 1,030,000 | Franchise | -
 |  | Waste generated in operation | 78,000
The scope 3 emission of Fast cars upstream and downstream are as follows:

## Slide 2: Competitor Analysis
This is high-level research into scope3 emissions targets seta by a selection of Fast Cars competitors.
Most of these targets are addressing the ‘use of products sold’ downstream emission category only.
This is because it is typically the greatest proportion of total scope 3 emission for automotive companies.
Only BMW Group is also addressing upstream emissions
Company | Scope 3 Emissions Reduction Target and actions
Nissan Motors Co.Ltd | Reduce scope 3 GHG emission from use of sold products 32.5% per vehicle kilometre over the same time frame
General Motors | Reduce scope 3 GHG emissions from use of sold products of light duty vehicles by 51% per vehicle kilometre by 2035 from 2018 base year
Ford Motor company | Reduce scope 3 use of sold product GHG emissions 50% per vehicle kilometre by 2035 from a 2019 base year
BMW group | Reduce scope 3 GHG emissions from use of sold product 40% per vehicle kilometre by 2030 from a 2019 base year Reduce scope 3 GHG emissions from purchased goods & services and upstream transportation & distribution services 22% per vehicle sold by 2030 from a 2019 base year
Volva Car group | Reduce scope 3 GHG emissions from use of sold product 52% per vehicle kilometre by 2030 from a 2019 base year

## Slide 3: Key initiatives for Fast Cars to consider
To be in line with the industry, we recommend that Fast Cars determine a target to address scope 3 use of product sold emissions. Some initial initiatives that could address these emissions are detailed below
Initiative | Initiative 1: Electric or Hybrid Vehicles | Initiative 2: Lighter Vehicles | Initiative 3: Actual Air Emission Data Collection
Description and rationale | This initiative has the greatest potential to reduce use of products sold, particularly if the vehicle is charged with renewable energy (zero emissions) | The heavier the vehicle the more fuel it uses. By investing in newer and better materials and material research and development, Fast cars could develop lighter vehicles that uses less fuel per kilometer | Fitting cars with air emissions monitors that feed into car information systems and tell the customer when their car may need a service or upgrade based on emission